## Slide 1
Bare Metall / Hardwareplattform
BUS-Controler
I/O
I/O
I/O
I/O BUS-Controller
(e.g. ET200SP)
Hypervisor Type 1 or 2 e.g. Linux with KVM idally with native Container Support .
Hypervisor-Web-Control-Panel
(if existent)
Contains only rudimentary logic for singal routing via onboard OPC-UA Server and minimal program logic for emergency operation and safe shutdown.
SoftPLC VM
(Windows Server)
Applikation VM
(headless Linux)
Only necessary if hypervisor has no native Container Support
Container Environment e.g. Docker
Visualization App - Container
SCADA App - Container
Database App - Container
. . .
NAS or USB-Storage
(can also be Cloud)
Acts as gate keeper, firewall and security instance. Performs authentication- and authorization checking and granting.
Security VM
(headless Linux)
Open WWW
Edge Device e.g. IPC
Sensor e.g. PT100
Actuators e.g. Solenoid-Valve
Modbus
OPC-UA
Modbus
TSDB
HTTP
HTTP
HTTPS
e.g. NFS
4…20 mA
+24 V
(Modbus and/or OPC-UA as backup if PLC dies)
Router
HTTPS
Multiple
OPC-UA
MQTT
SWITCH
Other BUS-Actuators
e.g. FC, Valves, …
Modbus
IoT-Concept Schema
Modbus (TCP/IP)
Backend Datanetwork (TCP/IP)
Backend Applicationnetwork (TCP/IP)
WWW-facing Applicationnetwork (TCP/IP)
Legend
Primary protocol
(fallback connection for emergency)
Control-Logic
. . .
Other „black box“ control systems
OPC-UA